Chemistry 30

# Unit 6: Redox Reactions and Electrochemistry

Assignment 2:  Balancing Redox Reactions						24

6	1.	Balance the following reactions using the oxidation number method.

a.	   NaClO   +      H2S   (      NaCl   +      H2SO4

|  | initial |  | final | change |  | Coefficient |  | Total e- |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cl | +1 | ( | -1 | 2 | ( | 4 | = | 8 |
| S | -2 | ( | +6 | 8 | ( | 1 | = | 8 |

4 NaClO   +     1 H2S   (    4  NaCl   +     1 H2SO4

b.	   Sn   +      HNO3   +      H2O   (      H2SnO3   +      NO

|  | initial |  | final | change |  | Coefficient |  | Total e- |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Sn | 0 | ( | +4 | 4 | ( | 3 | = | 12 |
| N | +5 | ( | +2 | 3 | ( | 4 | = | 12 |

3 Sn   +      4 HNO3   +     1 H2O   (      3 H2SnO3   +    4  NO

c.	     K2Cr2O7   +      SnCl2   +      HCl   (       CrCl3   +     SnCl4   +    KCl   +    H2O

|  | initial |  | final | change |  | no. atoms |  | No. e- |  | Coefficient |  | Total e- |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cr | +6 | ( | +3 | 3 | ( | 2 |  | 6 | ( | 1 | = | 6 |
| Sn | +2 | ( | +4 | 2 |  |  | = | 2 | ( | 3 | = | 6 |

1 K2Cr2O7   +  3 SnCl2   +  14 HCl   (  2 CrCl3  +  3 SnCl4 + 2 KCl  + 7 H2O

6	2.	Balance the following half-reactions. Be sure to balance for atoms first, then balance for charge by adding electrons to the appropriate side of the equation. Also identify each as either an oxidation or reduction.

a.	Br2		(    Br –			Br2 + 2 e- (   2  Br –		reduction

b.	Fe2+		(    Fe3+			Fe2+ (    Fe3+ + 1e-		oxidation

c.	MnO4– +  H+ 	(  Mn2+ +  H2O			MnO4– + 8 H+ + 5e- (  Mn2+ + 4 H2O	reduction

4	3.	Break each equation into two half-reactions.  Identify each half-reaction as oxidation or reduction.

a.	2 K + I2 ( 2 KI

2 K ( 2 K+ + 2 e-	oxidation

I2 + 2 e- ( 2 I-		reduction

b.	2 Br – + F2 ( Br2 + 2 F –

F2 + 2 e - ( 2 F–	reduction

2Br– ( Br2 + 2 e –	oxidation

4	4.	Balance the following reactions using the half-reaction method.

a.	Na + Br2 ( NaBr

| Step 1 | Step 2 | Step 3 |
| --- | --- | --- |
| Write the two balanced half-reactions, removing any spectator ions: | Balance for electrons | Add the half-reactions, replacing any spectator ions that were removed and/or recombining compounds |
| Na ( Na+ + 1 e– | ( 2 | 2Na ( 2Na+ + 2 e– |
| Br2 + 2 e – ( 2 Br – |  | Br2 + 2 e – ( 2 Br – |
| added together: | 2Na + Br2 ( 2Na+ + 2 Br – |
| reform compound: | 2 Na + Br2 ( 2 NaBr |

b.	CrO42- + H+ + Cl- ( Cr3+ + Cl2 + H2O

Remember to balance for atoms before adding electrons to balance for charge.

| Step 1 | Step 2 | Step 3 |
| --- | --- | --- |
| Write the two balanced half-reactions, removing any spectator ions: | Balance electrons | Add the half-reactions, replacing any spectator ions that were removed and/or recombining compounds |
| CrO42- + 8 H+ + 3e–( Cr3+ + 4 H2O | ( 2 | 2 CrO42- + 16 H+ + 6 e–( 2 Cr3+ + 8 H2O |
| 2 Cl – ( Cl2 + 2 e– | ( 3 | 6 Cl – ( 3 Cl2 + 6 e– |
| added together: | 2CrO42- + 16H+ + 6Cl – ( 2Cr3+ + 3Cl2 + 8H2O |

4	3.	Balance the following reactions using either the oxidation number method or the half-reaction method.

a.	NO + As + H2O ( N2O + HAsO2

|  | initial |  | final | change |  | no. atoms |  | No. e- |  | Coefficient |  | Total e- |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| N | +2 | ( | +1 | 1 | ( | 2 (in N2O) | = | 2 | ( | 3 | = | 6 |
| As | 0 | ( | +3 | 3 |  |  |  | 3 | ( | 2 | = | 6 |

Answer:	6 NO + 2 As +  H2O ( 3 N2O + 2 HAsO2

b.	Ce4+ + I– + OH– ( Ce3+ + IO3– + H2O

| Step 1 | Step 2 | Step 3 |
| --- | --- | --- |
| Write the two balanced half-reactions, removing any spectator ions: | Balance electrons | Add the half-reactions, replacing any spectator ions that were removed and/or recombining compounds |
| Ce4+ + 1 e– ( Ce3+ | ( 6 | 6Ce4+ + 6 e– ( 6Ce3+ |
| I– + 6 OH– ( IO3– + 3 H2O + 6 e– |  | I– + 6 OH– ( IO3– + 3 H2O + 6 e– |
| added together: | 6 Ce4+ + I– + 6 OH– ( 6 Ce3+ + IO3– + 3 H2O |